# Text boxes

# Top 10 List for Workplace Savings

6. Maintain HVAC system and use BMPs

Auto-setback thermostats adjust the settings (up or down) for evenings and weekends. Adjusting temperature settings by three or four degrees can produce savings of 10% or more.

7. Set water heater to appropriate temperature

Reducing the setting from 140 to 120 degrees could save over 18% of the energy used at the higher setting.

Even a 10-degree reduction will save more than 6% in water-heating energy.

8. Use energy efficient lamps and bulbs

T-8 lamps use 20% less energy than T-12. T-5 lamps are 10-15% more efficient than T-8. Compact fluorescent bulbs in exit signs use 20-30 watts and are 50% more efficient than incandescents. LED bulbs use 1-10 watts.

9. Install occupancy sensors for lighting

New technology offers better lighting, heating and office systems that are more energy efficient. Savings of 25% or more are typical. That equates to $4,000 in savings per year for a 10,000 ft2 office. In a small office where lights are left on unnecessarily for just two hours a day, the annual energy wasted is $10.

10. Use Energy Star rated electronics and appliances and turn them off when not in use

U.S. EPA Energy Star partners have cut operational costs for energy, water and paper products by 40% or more.

If every computer and monitor in the country were turned off at night, the U.S. could close eight large power stations and avoid emitting 7 million tons of CO2 a year. Energy Star printers can cut a printer’s electricity use by more than 65%.

## The Sustainable Office

1. Establish a green team

A team approach spreads the responsibility across your business and gives employees from different departments a chance to contribute ideas. A group effort also guards against the chance that the company’s efforts will cease with the departure of a single employee. The position of team leader can rotate or remain with one individual. Use your corporate culture as a guide to determine what will work best for your company.

2. Recycle, buy recycled and practice waste reduction

Go paperless or use paper with 30-100% post-consumer recycled content. One ton of 100% recycled paper saves the equivalent of 4,100 kWh of energy, 7,000 gallons of water, 60 pounds of air emissions, and three cubic yards of landfill space.

3. Use water-efficient landscaping practices

Change landscaping from lawns to native plants that don’t require additional irrigation. Watch the weather—if rain is forecast don’t water and turn off sprinklers when it starts. Don’t over water.

4. Repair leaks

A leaky toilet or dripping faucet can waste thousands of gallons of water a year. One dripping faucet can waste up to 20 gallons of water per day. If the drip is hot water, you’re paying for wasted energy too. A small, silent toilet leak can cost $50 per year in water and sewer costs.

5. Use low-flow toilets and faucet aerators

All new toilets are required to use 1.6 gallons or less per flush, while older models used up to 7 gallons. Aerators can cut faucet water use in half.